## Slide 1: CPSC 8810: Motion Planning Final Project
By- Kalpit Madhusudan Vadnerkar Vasanth Seethapathi
Project Title: Nonholonomic Motion Planning for a Car in 2D Environment using RRT*

## Slide 2: Problem and Approach
RRT* algorithm incrementally builds a tree of random configurations in the search space, similar to RRT, and attempts to rewire the tree iteratively by adding new connections between nodes resulting in a low-cost path optimized tree structure.
Develop an efficient RRT* algorithm to plan collision-free motion for a nonholonomic Dubins car through 2D obstacles, while considering its motion constraints.

## Slide 3: Operating Parameters
Car: Non Holonomic dubins Car, this contains the information of initial and final positions, as well as its motion constraints.
max_steps: Maximum number of steps the algorithm will take before terminating. It has an influence on the execution time and computational resources required for planning.
pick_target: Frequency at which the algorithm will select a new target node to expand the tree towards the goal. A higher value will result in more frequent expansions on contrary to a lower value which will result in fewer expansions.
check_dubins: This parameter checks for the direct dubins paths when adding new edges to the tree. Also, it expands the dubins analytic solution that connects to the final position if the solution is valid and collision free. This also sets a frequency to check for connecting to the final position.
search_radius: Maximum distance the algorithm will search for nodes to connect while expanding the tree. A larger value will result in wider search area.

## Slide 4: RRT and RRT* comparison
RRT
RRT*
Note: Based on sampling points, the trajectory is expected to vary from one simulation run to another
Random Seeds are set to the same value for repeatability of results for comparison.

## Slide 5: 2D map exploration based on Iterations on RRT* -
Parameters: max_steps=50, pick_target=10, check_dubins=1, search_radius=1.0

## Slide 6: Algorithm Comparison -
Hybrid A*
RRT
RRT*
Note: Based on sampling points, the trajectory is expected to vary from one simulation run to another

## Slide 7: Benefits -
RRT* handles the complex environment that has multiple obstacles, narrow passages, or multiple paths to a goal. And, also RRT* can handle dynamic environment but A* assumes a static environment and can be inefficient when there are frequent changes.
RRT* can optimize the path cost by iteratively improving the solution until it reaches the optimal path. A* provides a solution that is optimal but need not be the shortest path.
Both RRT* and RRT are probabilistically complete algorithms – they guarantee a solution if one exists, with high probability. However, RRT* has a stronger completeness guarantee. Also it can achieve higher convergence as the tree expansion is guided towards goal region using a heuristic estimate.

## Slide 8: Drawbacks -
Although RRT* can find a feasible solution with a certain probability, it may not always find the optimal solution and its quality may vary based on the problem and environment.
RRT* may not be suitable for problems that involve multiple agents or goals that require coordination, as it is designed for motion planning problems with a single start and goal configuration.
Choosing optimal values for parameters such as step size, sampling density, and exploration radius can be challenging and require significant experimentation due to RRT*'s sensitivity to parameter choices.
The drawback of using graph-search techniques for trajectory generation is the resolution lost due to discretization of state space and/or control space. The only boundary states that can be reached are those that already exist in the network.

## Slide 9: Path Smoothing Methods -
Kalman Filtering
Polynomial Fitting
Spline based Smoothing

## Slide 10: Success rate : depends on the